## Slide 1
LSTM with Dual Adaptive Conformal Prediction
Streamflow Uncertainty Quantification Across Five Snowmelt-Dominated Watersheds
Pranav Cheedalla & Austin Santhakumar
RIDE Research | Spring 2026

## Slide 2
Presentation Overview
• Problem Statement — Why streamflow prediction matters and the challenge of snowmelt hydrology
• Study Sites & Data — Five watersheds, 1,461 daily observations each (2019–2022)
• LSTM Architecture — Model design, training configuration, and key features
• Model Performance — R², RMSE, MRE, NSE across all sites
• DACP Method — Dual adaptive regulators for prediction intervals
• Coverage Experiments — 70%, 80%, 90%, 95% targets across all sites
• Per-Site Analysis — Detailed results and hydrographs for each watershed
• Conclusion & Future Work — Key findings and next steps

## Slide 3
01
Problem Statement

## Slide 4
Why Streamflow Prediction Matters
• Snowmelt-driven watersheds provide critical water supply for agriculture, municipalities, and ecosystems across the Western U.S.
• Water Resource Management — Reservoir operations, irrigation scheduling, and drought planning require accurate daily forecasts
• Flood Warning — Peak discharge events can cause devastating damage if not anticipated in advance
• Ecological Monitoring — Aquatic ecosystems depend on minimum flow thresholds for survival
• Current Limitation — Deep learning models produce only point predictions without confidence measures, limiting operational decision-making

## Slide 5
The Challenge: Snowmelt Hydrology
• Snowmelt hydrology is highly nonlinear: discharge depends on SWE, temperature, precipitation history, and soil moisture
• Time-dependent interactions — snowpack accumulates over weeks but can melt in days
• Regime shifts — the same watershed behaves differently during snowmelt season vs. rain-on-snow vs. baseflow
• Traditional models struggle to capture these complex temporal dependencies
• Our Approach — Standard LSTM for point prediction + Dual Adaptive Conformal Prediction (DACP) for distribution-free uncertainty quantification

## Slide 6
02
Study Sites & Data

## Slide 7
Five Snowmelt-Dominated Watersheds
• Bunchgrass Meadow — High-flow, snowmelt-dominated (161–2,922 cfs). Widest dynamic range; log transform required
• Easy Pass — High-flow, glacial/snow (2–277 cfs). High-elevation alpine; rapid solar-driven melt onset
• Paradise — Mid-flow, rain-on-snow (0–79 cfs). Flashy events produce sharp discharge spikes; hardest timing to predict
• Swift Creek — Low-flow, complex (1–171 cfs). Mixed hydrology with low baseflow and occasional sharp peaks
• Touchet — Low-flow, rain-dominant (0–672 cfs). Stable baseflow punctuated by one dominant extreme peak event
• All sites: 1,461 daily observations (2019–2022), Western U.S.

## Slide 8
Input Features: 10 Variables × 14-Day Window
• Base Features (6): WESD (Snow Water Equivalent), GHI (Global Horizontal Irradiance), PRCP (Precipitation), SNWD (Snow Depth), TAVG (Average Temperature), DISCHRG_LAG (Previous Day's Discharge)
• Engineered Feature: prcp_7d — 7-Day Cumulative Precipitation. Rolling sum capturing antecedent wetness; rising values signal incoming discharge spikes
• Engineered Feature: API — Antecedent Precipitation Index. Exponentially-weighted sum (α=0.08 decay) representing soil wetness state
• Engineered Features: sin(day of year) & cos(day of year) — Circular seasonal encoding providing smooth annual signal without Jan→Dec discontinuity
• DISCHRG_LAG provides strong autoregressive signal during recession periods

## Slide 9
03
LSTM Model Architecture

## Slide 10
LSTM Architecture & Training
• Two Stacked LSTM Layers — 128 hidden units per layer capturing temporal dependencies over 14-day input window
• Fully Connected Head — 128 → 64 → 32 with ReLU activations and dropout 0.2 for regularization
• Output — Single predicted discharge value in normalized scale, inverse-transformed to physical units (cfs)
• Loss Function — Huber loss (δ = 1.0) applied uniformly across all sites. Transitions from quadratic (MSE-like) for small errors to linear (MAE-like) for large errors
• Critical for extreme peaks: prevents rare events (Bunchgrass ~2,922 cfs, Touchet ~672 cfs) from dominating gradient signal
• Log(1+Q) transform applied to Bunchgrass Meadow and Paradise to stabilize heavy-tailed distributions

## Slide 11
Training Configuration
• Optimizer: Adam (lr = 1e-3) with gradient clipping (max norm = 1.0)
• Train / Test Split: 85% / 15% chronological (~1,241 training, ~220 test samples per site)
• Validation: 10% of training window for early stopping
• Max Epochs: 200 | Early Stopping Patience: 25 epochs
• Batch Size: 32 | Random Seed: 42 (fixed for reproducibility)
• Scalers fit only on training data to prevent data leakage
• No physics-informed loss terms (λ = 0) — model learns purely from data
• No attention mechanism — relies on LSTM memory cell alone

## Slide 12
04
Model Performance

## Slide 13
Overall LSTM Model Performance
Site | R² | RMSE (cfs) | MRE | NSE | Loss Function
Bunchgrass Meadow | 0.954 | 166.31 | 0.201 | 0.954 | Huber δ=1.0
Easy Pass | 0.616 | 13.05 | 0.371 | 0.616 | Huber δ=1.0
Paradise | 0.838 | 2.27 | 0.360 | 0.838 | Huber δ=1.0
Swift Creek | 0.405 | 3.84 | 0.173 | 0.405 | Huber δ=1.0
Touchet | 0.821 | 11.08 | 0.758 | 0.821 | Huber δ=1.0

## Slide 14
Performance Analysis
• Best Performer: Bunchgrass Meadow — R² = 0.954, NSE = 0.954. Captures dominant seasonal snowmelt signal with high fidelity. RMSE of 166.31 cfs is only ~5.7% of peak discharge range.
• Strong Performer: Paradise — R² = 0.838 despite flashy rain-on-snow events. Log transform stabilizes heavy-tailed distribution.
• Strong Performer: Touchet — R² = 0.821 but extremely high MRE = 0.758. Model has proportionally large errors during baseflow periods (1–5 cfs).
• Moderate: Easy Pass — R² = 0.616. 14-day window insufficient for rapid solar-driven melt onset; systematic underestimation during May-June peaks.
• Most Challenging: Swift Creek — R² = 0.405. Irregular multi-peaked glacial pattern with summer melt spikes independent of precipitation. However, best MRE = 0.173 — predictions proportionally close to observed values.

## Slide 15
Understanding RMSE & MRE
• RMSE (Root Mean Squared Error) — Scale-dependent average error magnitude in discharge units (cfs). Must be compared to site's discharge range.
• Bunchgrass's 166.31 cfs appears large but is only ~5.7% of max (2,922 cfs). Swift Creek's 3.84 cfs seems small but is ~2.2% of max (171 cfs).
• MRE (Mean Relative Error) — Scale-independent metric normalizing errors by observed value. MRE = 0.201 means predictions are off by ~20% on average.
• Swift Creek has best MRE (0.173) despite worst R² — errors are small relative to observed values during dominant low-flow regime.
• Touchet has worst MRE (0.758) — while RMSE is low (11.08 cfs), proportional errors during baseflow are severe.
• No single metric tells the whole story — always interpret together in context of each site's discharge scale and hydrological regime.

## Slide 16
05
Dual Adaptive Conformal Prediction (DACP)

## Slide 17
Why Uncertainty Quantification?
• Point Predictions Are Not Enough — A prediction of 'tomorrow's flow = 45 cfs' gives no indication of confidence
• Is it 45 ± 2 cfs? Or 45 ± 50 cfs? Decision-makers need to know how much to trust each prediction
• Critical during regime transitions (snowmelt onset, rain-on-snow events) when prediction errors are largest
• DACP wraps any point-prediction model with adaptive prediction intervals — distribution-free, no Gaussian assumptions
• Adaptive — intervals respond to model accuracy in real-time. Coverage guarantees — e.g., 95% of true values fall within bounds
• Key advantage: works with any base model, requires no parametric assumptions about error distribution

## Slide 18
DACP: Building Prediction Intervals
• Step 1: Collect Error History — Compute |actual − predicted| for past 180 days (rolling window). Fixed-size set of recent errors.
• Step 2: Partition via t_m Regulator — Data partitioning regulator controls what fraction of error history feeds into calibration vs. reference. t_m = 0.35 means upper 35% provides calibration residuals.
• Step 3: Compute Interval Half-Width — Take the (1 − α_m)-quantile from calibration set. This quantile q becomes the half-width of prediction interval.
• Step 4: Prediction Interval — [max(ŷ − q, 0), ŷ + q]. Floor at 0 enforces physical non-negativity of discharge.
• 180-day rolling window → partition → quantile → [max(ŷ − q, 0), ŷ + q]
• Distribution-free, adaptive, and requires no parametric assumptions

## Slide 19
DACP: Dual Adaptive Regulators
• Data Partitioning Regulator (t_m) — Controls how much error history goes to calibration vs. reference:
• • If covered: t_{m+1} = t_m + γ · μ₁ (μ₁ = 0.03, slow adjustment — ~33 observations to shift meaningfully)
• • If missed: t_{m+1} = t_m − γ · μ₂ (μ₂ = 0.50, fast reaction — ~2 misses trigger significant widening)
• • μ₂ / μ₁ ≈ 17× asymmetry — reacts aggressively to misses but adjusts slowly after coverage
• Quantile Regulator (α_m) — Controls quantile level for interval half-width:
• • α_{m+1} = α_m + k_adap · (α_target − e_m) where e_m = 1 if missed, 0 if covered
• • k_adap = 0.005 (very small) — ensures slow quantile updates to prevent oscillation
• Fine-grained width control via α_m; structural error distribution shifts handled by t_m

## Slide 20
DACP Parameter Configuration
• Rolling Window (n): 180 days — ≈80 calibration points for stable quantile estimation with temporal relevance
• t_m Initial: 0.35 — 65% of error history discarded; upper 35% enters calibration (focus on recent, high-magnitude errors)
• t_m Bounds: [0.10, 0.60] — Calibration fraction bounded between 40–90%
• μ₁ (covered): 0.03 — Slow: gradual interval tightening after successful coverage
• μ₂ (missed): 0.50 — Fast: aggressive interval widening after misses
• α_target: 1 − coverage target (0.05 for 95%, 0.10 for 90%, 0.20 for 80%, 0.30 for 70%)
• k_adap: 0.005 (constant across all targets) — conservative choice; paper recommends per-target tuning
• All parameters fixed uniformly across all 5 sites — tests DACP generalization across diverse flow regimes

## Slide 21
06
Coverage Experiments & Results

## Slide 22
DACP Coverage Results: All Sites × All Targets
Site | 70% Target | 80% Target | 90% Target | 95% Target
Bunchgrass Meadow | 70.9% | 80.5% | 88.6% | 92.7%
Easy Pass | 72.3% | 79.5% | 87.7% | 91.4%
Paradise | 54.1% | 68.2% | 83.6% | 89.5%
Swift Creek | 68.6% | 79.5% | 86.8% | 91.8%
Touchet | 64.5% | 75.9% | 87.3% | 91.8%

## Slide 23
Coverage Performance Analysis
• Three sites achieve relatively close coverage (Bunchgrass Meadow, Easy Pass, Swift Creek) — track targets well at 70% and 80%
• Systematic under-coverage at higher targets (90%, 95%) reflects LSTM's tendency to underestimate extreme flows
• Paradise shows most severe under-coverage: 54.1% at 70% target (−15.9%), 68.2% at 80% (−11.8%)
• Touchet shows consistent moderate under-coverage across all targets: −5.5% at 70%, −4.1% at 80%, −2.7% at 90%, −3.2% at 95%
• Key differentiating factor: ratio of extreme-event residuals to typical residuals. When peaks produce residuals 5–10× larger than baseflow, a single rolling-window quantile cannot cover both regimes
• Constant k_adap = 0.005 (vs. paper-recommended per-target schedule) contributes to slow convergence and under-coverage

## Slide 24
Average Interval Widths Across Targets
Site | 70% Width | 80% Width | 90% Width | 95% Width
Bunchgrass Meadow | 365.23 cfs | 441.52 cfs | 533.31 cfs | 599.08 cfs
Easy Pass | 14.65 cfs | 19.45 cfs | 24.36 cfs | 31.06 cfs
Paradise | 1.77 cfs | 2.48 cfs | 3.76 cfs | 5.55 cfs
Swift Creek | 1.77 cfs | 2.26 cfs | 4.10 cfs | 9.91 cfs
Touchet | 9.91 cfs | 12.53 cfs | 18.40 cfs | 27.69 cfs

## Slide 25
Interval Width Analysis
• Width increases monotonically with coverage target as expected — DACP correctly trades precision for coverage
• Bunchgrass Meadow shows widest absolute intervals (599 cfs at 95%) reflecting extreme dynamic range, but reasonable relative to peak discharge
• Swift Creek: width grows dramatically from 1.77 cfs (70%) to 9.91 cfs (95%) — 5.6× expansion reflecting erratic glacial pattern
• Paradise maintains tightest absolute intervals (5.55 cfs at 95%) but insufficient for flash-event peaks — only ~7% of peak discharge
• Touchet: 27.69 cfs at 95% represents ~4.1% of maximum discharge — tightest relative interval of all sites
• Normalized widths (as % of mean discharge) show DACP adapts proportionally to each site's scale

## Slide 26
07
Per-Site Analysis

## Slide 27
Bunchgrass Meadow — Best Overall Performance
• R² = 0.954 | RMSE = 166.31 cfs | MRE = 0.201 | NSE = 0.954
• Highest-flow site with extreme dynamic range (mean 716 cfs, max 2,922 cfs). Log(1+Q) transform stabilizes training.
• LSTM captures dominant seasonal signal: spring melt peaks and summer recession curves with high fidelity
• DACP Coverage: Strong at 70% (70.9%) and 80% (80.5%). Falls below at 90% (88.6%, −1.4%) and 95% (92.7%, −2.3%)
• Most misses occur at peak timing events — model slightly lags sharpest spring rises. DISCHRG_LAG helps recession but cannot anticipate sudden melt-onset accelerations.
• Interval width of 599 cfs at 95% is substantial in absolute terms but reasonable relative to site's extreme flow range

## Slide 28
Easy Pass — Moderate Performance, Strong Coverage
• R² = 0.616 | RMSE = 13.05 cfs | MRE = 0.371 | NSE = 0.616
• High-elevation alpine site: near-zero winter flow to sharp melt-driven spikes (max 277 cfs, mean 22 cfs)
• Model captures broad seasonal pattern but systematically underestimates during May-June peak events — 14-day window insufficient for rapid solar-driven melt onset
• DACP Coverage: Tracks closely at 70% (72.3%, +2.3%) and 80% (79.5%, −0.5%). Under-tracks at 90% (−2.3%) and 95% (−3.6%)
• Under-coverage at higher targets attributable to systematic peak underestimation: rolling window calibration from stable periods insufficient for spring extremes
• Asymmetric μ₂ update partially compensates, but 180-day window warm-up limits rapid widening at melt season start

## Slide 29
Paradise — Most Challenging Coverage
• R² = 0.838 | RMSE = 2.27 cfs | MRE = 0.360 | NSE = 0.838
• Mixed rain-on-snow site with rapid-response hydrology: sharp, brief discharge spikes (max 79 cfs, mean 5.25 cfs)
• Most challenging DACP coverage in study — systematic under-coverage at all targets: 54.1% at 70% (−15.9%), 68.2% at 80% (−11.8%)
• Two contributing factors: (1) Most frequent and rapid flash events — ascend and recede within 1–3 days. 14-day window captures seasonal signal but not exact timing.
• (2) Small absolute scale (mean 5.25 cfs) means modest absolute errors translate to narrow physical intervals — 5.55 cfs at 95% is only ~7% of peak
• Potential solutions: longer rolling window, site-specific k_adap, or asymmetric upper-bound construction during high prcp_7d periods

## Slide 30
Swift Creek — Weak Predictions, Strong Uncertainty
• R² = 0.405 | RMSE = 3.84 cfs | MRE = 0.173 (best) | NSE = 0.405
• Most challenging predictive site: discharge 0–171 cfs, predominantly below 10 cfs (mean 3.73 cfs)
• Irregular multi-peaked glacial pattern — summer melt produces erratic spikes independent of precipitation. Fundamentally difficult with precipitation-feature-based model.
• Best MRE (0.173) despite worst R² — model accurately represents dominant low-flow regime even while missing peak timing
• DACP Coverage: Stable and noteworthy — 68.6% at 70% (−1.4%), 79.5% at 80% (−0.5%), 86.8% at 90% (−3.2%), 91.8% at 95% (−3.2%)
• Key insight: DACP provides useful uncertainty bounds even when base model accuracy is moderate — compensates by widening intervals proportionally to accumulated errors

## Slide 31
Touchet — High R², Systematic Under-Coverage
• R² = 0.821 | RMSE = 11.08 cfs | MRE = 0.758 (worst) | NSE = 0.821
• Moderate discharge range (mean 18.75 cfs, max 672 cfs) dominated by one or two massive annual peaks (~100–672 cfs)
• Extreme peak-to-baseflow ratio is defining challenge: stable 5–30 cfs punctuated by rare extreme events
• Huber loss critical — prevents dominant peak from overpowering gradients from hundreds of stable low-flow days
• High MRE (0.758) reflects frequent proportionally large errors during baseflow periods (1–5 cfs)
• DACP Coverage: Consistent moderate under-coverage across all targets: 64.5% at 70% (−5.5%), 75.9% at 80% (−4.1%), 87.3% at 90% (−2.7%), 91.8% at 95% (−3.2%)
• Primary cause: 180-day window mixes small baseflow residuals with large peak residuals — quantile is intermediate, too wide for low-flow and too narrow for extremes

## Slide 32
08
Discussion

## Slide 33
Discussion: Model Accuracy
• Sites with sustained, slow-varying snowmelt regimes (Bunchgrass Meadow, Touchet) predicted with highest accuracy
• DISCHRG_LAG feature provides strong autoregressive signal during recession periods — explains much of high R² at these sites
• Sites with rapid-response hydrology present greater challenges: Paradise flash events, Easy Pass abrupt melt onset, Swift Creek glacial irregularity
• Increasing input window beyond 14 days may improve gradual snowpack dynamics prediction (Moghaddasi et al. 2025 suggests 60–90 day optimal lookbacks)
• However, longer windows would not address sub-daily flash events — Paradise timing errors are fundamentally about precipitation-event timing, not snowpack accumulation
• Log transform essential for heavy-tailed sites (Bunchgrass, Paradise) — without it, raw values spanning 0–2,922 cfs compress low-flow information

## Slide 34
Discussion: DACP Coverage Performance
• Three sites achieve relatively close coverage (Bunchgrass, Easy Pass, Swift Creek); two show systematic under-coverage (Paradise, Touchet)
• Key differentiator: ratio of extreme-event residuals to typical residuals. When peaks produce residuals 5–10× larger than baseflow, single quantile cannot cover both regimes
• Constant k_adap = 0.005 is more conservative than paper-recommended per-target schedule (0.05 for 95%, scaling to 0.30 for 70%)
• Conservative k_adap means α_m adapts very slowly — requires more observations to converge. Explains consistent under-coverage at higher targets
• Asymmetric μ₂/μ₁ ratio of 0.50/0.03 ≈ 17× is essential for responsive coverage — correctly treats cost of missing as far greater than cost of marginally wide intervals
• Walk-forward rolling retraining would accumulate more calibration history, helping DACP better represent full residual distribution including rare extremes

## Slide 35
09
Conclusion & Future Work

## Slide 36
Key Findings
• Point Prediction: Standard LSTM achieves R² from 0.405 (Swift Creek) to 0.954 (Bunchgrass Meadow). Performance strongly depends on hydrological regime complexity.
• DISCHRG_LAG is critical for autoregressive accuracy in slow-varying snowmelt regimes — provides strong recession curve signal
• Huber loss (δ=1.0) effectively prevents extreme-peak dominance during training — essential for sites with heavy-tailed discharge distributions
• DACP provides adaptive prediction intervals with coverage tracking targets well on three sites (Bunchgrass, Easy Pass, Swift Creek)
• Systematic under-coverage at Paradise and Touchet due to extreme multi-scale residual distributions — single quantile cannot simultaneously cover baseflow and peak regimes
• DACP provides useful uncertainty bounds even when base model accuracy is moderate (Swift Creek: 91.8% coverage despite R²=0.405)

## Slide 37
Limitations
• No attention mechanism — relies solely on LSTM memory cell; multi-head attention could weight critical time steps
• Uniform hyperparameters across all sites — no site-specific loss function optimization or feature selection
• Short test window (15% ≈ 220 days) — limited exposure to full range of hydrological variability
• Fixed train/test split rather than walk-forward rolling retraining — model does not adapt to evolving watershed conditions
• Constant k_adap = 0.005 across all coverage targets — more conservative than reference paper recommendations
• Single loss function (Huber) for all sites — NSE loss may better suit Touchet; asymmetric upper-bound construction may better suit Paradise

## Slide 38
Future Work
• Per-target k_adap values as specified in Zong et al. (2026): 0.05 for 95%, scaling up to 0.30 for 70% — faster α_m convergence, likely closing under-coverage gap
• Walk-forward rolling retraining strategy — accumulate more calibration history and adapt to evolving watershed conditions
• Longer input sequences (30–60 days) — better capture slow snowpack accumulation dynamics, particularly for glacial sites like Swift Creek
• Multi-head attention mechanism (4 heads) — weight critical time steps in input window, as used in PI-LSTM reference
• Site-specific loss function optimization: NSE loss for Touchet, asymmetric upper-bound construction for Paradise flash events
• Hybrid physics-informed loss terms — incorporate water balance constraints (λ > 0) for snowmelt hydrology regularization
• Extended calibration window (180–360 days with walk-forward retraining) — better represent full residual distribution

## Slide 39
Thank You
LSTM + DACP: Streamflow Prediction with Uncertainty Quantification
Pranav Cheedalla & Austin Santhakumar
RIDE Research | Spring 2026

## Slide 40
References
• Moghaddasi, Pouya, Keyhan Gavahi, and Hamid Moradkhani. 2025. 'Snow Drought to Hydrologic Drought Progression Using Machine Learning and Probabilistic Analysis.' Scientific Reports 15.
• Zong, Yuwei, Sobhan Badakhshan, Jie Zhang, and Yanwen Xu. 2026. 'Trustworthy Uncertainty Quantification via Distributionally-Robust Dual Adaptive Conformal Prediction.' Journal of Mechanical Design.
• Complete code (lstm_dacp_final.py), all 20 result CSVs (LSTM_SiteName_Target.csv), and per-site plots available in Final Result folder.