## Slide 1
LSTM + DACP
Standard Deep Learning with
Dual Adaptive Conformal Prediction
Streamflow Prediction & Uncertainty Quantification
Across 5 Snowmelt-Driven Watersheds
RIDE Research
May 2026

## Slide 2
Presentation Overview
01
Problem Statement
Why streamflow prediction matters and the challenge
02
Study Sites & Data
5 watersheds, 1,461 daily observations each
03
LSTM Architecture
Model design, training, and configuration
04
Model Performance
R², RMSE, MRE, NSE — per site
05
DACP Method
Dual adaptive regulators for prediction intervals
06
Coverage Experiments
70%, 80%, 90%, 95% across all sites
07
Per-Site Analysis
Plots, metrics, and discussion for each watershed
08
Conclusion & Deliverables
Summary and what we produced

## Slide 3
SECTION 1
Problem Statement

## Slide 4
Why Streamflow Prediction Matters
The Problem
Snowmelt-driven watersheds provide critical water supply for agriculture, municipalities, and ecosystems across the Western U.S.
Accurate daily streamflow forecasting is essential for:
Water resource management — reservoir operations, irrigation scheduling, and drought planning.
Flood warning — peak discharge events can cause devastating damage if not anticipated.
Ecological monitoring — aquatic ecosystems depend on minimum flow thresholds.
The Challenge
Snowmelt hydrology is highly nonlinear. Discharge depends on SWE, temperature, precipitation history, and soil moisture.
Traditional models struggle because:
Time-dependent interactions — snowpack accumulates over weeks but can melt in days.
Regime shifts — the same watershed behaves differently during snowmelt season vs. rain-on-snow vs. baseflow.
Our approach: Standard LSTM for point prediction + DACP for distribution-free uncertainty quantification.

## Slide 5
SECTION 2
Study Sites & Data

## Slide 6
Five Snowmelt-Dominated Watersheds
All sites: 1,461 daily observations (2019–2022), Western U.S.
Bunchgrass Meadow
High-flow, snowmelt-dominated
161 – 2,922 cfs
Widest dynamic range; snowmelt-dominated with extreme spring peaks. Log transform required.
Easy Pass
High-flow, glacial/snow
2 – 277 cfs
High-elevation alpine; rapid solar-driven (GHI) melt onset in spring.
Paradise
Mid-flow, rain-on-snow
0 – 79 cfs
Flashy rain-on-snow events produce sharp discharge spikes; hardest timing to predict.
Swift Creek
Low-flow, complex
1 – 171 cfs
Complex mixed hydrology with low baseflow and occasional sharp peaks.
Touchet
Low-flow, rain-dominant
0 – 672 cfs
Stable low baseflow punctuated by one dominant extreme peak event.

## Slide 7
Input Features
Each site uses 8 input features in a 14-day sliding window. Four key engineered features explained below.
Base Features (5)
WESD — Water Equivalent Snow Depth. Primary snowpack indicator; leading driver of spring runoff timing.
GHI — Global Horizontal Irradiance. Solar energy input; critical for glacial and alpine melt onset.
PRCP — Daily Precipitation. Direct water input; rain-on-snow events captured here.
SNWD — Snow Depth. Physical snowpack depth complement to WESD.
TAVG — Average Temperature. Temperature threshold for snowmelt onset (above 0°C).
Engineered Features (3)
prcp_7d — 7-Day Cumulative Precipitation. Rolling sum capturing recent soil saturation. A rising prcp_7d signals an incoming discharge spike.
doy_sin — Day-of-Year Sine. Seasonal encoding; peaks in spring (~day 91). Tells the model "where in the year" without a harsh Jan→Dec jump.
doy_cos — Day-of-Year Cosine. Seasonal encoding complement; together with sine, encodes a full circular calendar — all four seasons, no ambiguity.

## Slide 8
SECTION 3
LSTM Model Architecture

## Slide 9
Model Architecture: Standard LSTM
Architecture
Two Stacked LSTM Layers
128 hidden units per layer. Captures temporal dependencies over a 14-day input window.
Fully Connected Layers
128 → 64 → 32 with ReLU, dropout 0.2. Outputs single scalar discharge prediction.
Loss Function
Huber loss (δ = 1.0) applied uniformly across all sites. Robust to outlier discharge peaks.
No Physics Term
Unlike PI-LSTM, no water balance constraint (λ = 0). The model learns purely from data.
No Attention Mechanism
Relies on LSTM memory cell alone — no multi-head attention.
Key Differences from PI-LSTM
No Water Balance Constraint
PI-LSTM penalizes water balance violations with site-specific λ. Standard LSTM uses λ = 0 everywhere.
No Multi-Head Attention
PI-LSTM uses 4-head attention to weight critical time steps. Standard LSTM relies on LSTM memory only.
Uniform Hyperparameters
PI-LSTM uses Optuna-tuned site-specific loss functions and feature sets. Standard LSTM applies identical settings to all sites.
Uniform Loss Function
PI-LSTM selects NSE/MSE/Huber per site. Standard LSTM uses Huber δ=1.0 for all sites.

## Slide 10
Training Configuration
Parameter | Value
Input window | 14 days
LSTM layers | 2 × 128 hidden units
Dropout | 0.2
Loss function | Huber (δ = 1.0)
Optimizer | Adam (lr = 1e-3)
Gradient clipping | 1.0
Train / Test split | 85% / 15% (chronological)
Validation split | 10% of training window
Max epochs | 200
Early stopping patience | 25 epochs
Batch size | 32
Random seed | 42 (fixed)
LSTMModel (PyTorch)
class LSTMModel(nn.Module):
def __init__(self, n_features):
self.lstm = nn.LSTM(
n_features, 128, 2,
batch_first=True,
dropout=0.2)
self.fc = nn.Sequential(
nn.Linear(128, 64),
nn.ReLU(),
nn.Dropout(0.2),
nn.Linear(64, 32),
nn.ReLU(),
nn.Linear(32, 1))
def forward(self, x):
out, _ = self.lstm(x)
return self.fc(
out[:, -1, :]).squeeze(-1)

## Slide 11
SECTION 4
Model Performance

## Slide 12
LSTM Performance Summary
Site | RMSE (cfs) | MRE | R² | NSE | 95% Cov. | Avg Width
Bunchgrass Meadow | 559.31 | 0.428 | 0.476 | 0.476 | 86.4% | 1136.48
Easy Pass | 13.09 | 0.385 | 0.613 | 0.613 | 91.8% | 27.57
Paradise | 3.47 | 0.492 | 0.622 | 0.622 | 89.5% | 7.27
Swift Creek | 4.57 | 0.229 | 0.158 | 0.158 | 87.3% | 6.27
Touchet | 20.61 | 0.583 | 0.381 | 0.381 | 90% | 34.37
14-day rolling input, walk-forward prediction, uniform hyperparameters across all sites. No lagged discharge feature.
Best Performer: Paradise
R² = 0.622 — captures 62% of daily variance. Huber loss handles outlier peaks across all sites uniformly.
Most Challenging: Swift Creek
R² = 0.158 — complex mixed hydrology. But best MRE (0.229) — errors are small relative to observed values.

## Slide 13
Understanding RMSE & MRE
RMSE (Root Mean Squared Error)
Average error magnitude in the same units as discharge (cfs). Scale-dependent — you must compare to the site's discharge range.
Bunchgrass's 559.31 cfs looks huge — but on a site ranging 161–2,922 cfs, it's only ~19% of max.
Swift Creek's 4.57 cfs seems small — but on a site that only reaches ~171 cfs, it's ~2.7% of max.
RMSE alone cannot compare sites — you need scale context.
MRE (Mean Relative Error)
Normalizes errors by observed value — scale-independent. MRE = 0.428 means predictions are off by ~43% on average.
Swift Creek has best MRE (0.229) despite worst R² — errors are small in absolute terms relative to observed values.
Paradise has worst MRE (0.492) — flashy rain-on-snow spikes cause large relative errors even when absolute errors are small.
No single metric tells the whole story — always interpret together in context of each site's discharge scale.

## Slide 14
Comparison with PI-LSTM Reference
Site | LSTM R² | PI-LSTM R² | ΔR² | Key Insight
Bunchgrass Meadow | 0.476 | 0.79 | -0.314 | Physics loss + NSE critical for extreme range
Easy Pass | 0.613 | 0.545 | +0.068 | LSTM outperforms; Huber + attention hurt here
Paradise | 0.622 | 0.677 | -0.055 | Physics term improves rain-on-snow timing
Swift Creek | 0.158 | 0.276 | -0.118 | Neither model handles complex hydrology well
Touchet | 0.381 | 0.893 | -0.512 | Huber + site-specific λ essential for peak
Key Takeaway: Physics-Informed Gap
The standard LSTM underperforms the PI-LSTM reference at all sites except Easy Pass (ΔR² = +0.068), confirming that physics-informed training provides meaningful regularization for snowmelt hydrology.
The largest performance gaps are at Bunchgrass Meadow (ΔR² = −0.314) and Touchet (ΔR² = −0.512), where the PI-LSTM's physics loss and Huber objective are most critical.

## Slide 15
SECTION 5
Dual Adaptive Conformal Prediction (DACP)

## Slide 16
Why Uncertainty Quantification?
Point Predictions Are Not Enough
A prediction of "tomorrow's flow = 45 cfs" gives no indication of confidence.
Is it 45 ± 2 cfs? Or 45 ± 50 cfs?
Decision-makers — flood managers, reservoir operators, ecologists — need to know how much to trust each prediction. Without uncertainty bounds, they cannot properly assess risk.
This is especially critical during regime transitions (snowmelt onset, rain-on-snow events) when prediction errors are largest.
DACP wraps any point-prediction model with adaptive prediction intervals.
Distribution-free — no Gaussian assumptions. Adaptive — intervals respond to model accuracy. Coverage guarantees — e.g., 95% of true values fall within bounds.

## Slide 17
DACP: Building Prediction Intervals
At each time step, DACP uses past prediction errors to build an interval around the new prediction:
Step 1: Collect Error History
Compute |actual − predicted| for the past 180 days (rolling window). This gives a fixed-size set of recent errors.
Step 2: Partition via t_m Regulator
The data partitioning regulator t_m controls what fraction of error history feeds into calibration vs. reference.
Step 3: Compute the Interval Half-Width
Take the (1 − α_m)-quantile from the calibration set. This quantile q becomes the half-width of the prediction interval.
Step 4: Prediction Interval
[max(ŷ − q, 0), ŷ + q] — the floor at 0 enforces physical non-negativity of discharge.
180-day rolling window → partition → quantile → [max(ŷ − q, 0), ŷ + q]
Distribution-free, adaptive, and requires no parametric assumptions

## Slide 18
DACP: Dual Adaptive Regulators
After observing the true value, DACP updates both regulators:
Data Partitioning Regulator (t_m)
Controls how much of the error history goes to calibration vs. reference.
If covered:
t_{m+1} = t_m + γ · μ₁
(μ₁ = 0.03, slow adjustment)
If missed:
t_{m+1} = t_m + γ · μ₂
(μ₂ = 0.50, fast reaction)
μ₂ / μ₁ ≈ 17× — the algorithm reacts fast to misses but slowly when covered. This asymmetry is key to DACP's performance.
Quantile Regulator (α_m)
Controls the quantile level used to compute interval half-width.
Update rule:
α_{m+1} = α_m + λ(α* − e_m)
where e_m is the error indicator:
• e_m = 1 if missed
• e_m = 0 if covered
λ = 0.01 — ensures very slow quantile updates to prevent oscillation.
The quantile regulator provides fine-grained control over interval width, while the partitioning regulator handles structural shifts in error distribution.

## Slide 19
DACP Parameter Choices
Fixed parameters applied uniformly across all sites:
Parameter | Value | Rationale
Rolling window (n) | 180 days | ≈80 calibration points — stable quantile estimation with temporal relevance
t_m initial | 0.35 | 65% of error history enters calibration — stable quantiles
t bounds | [0.10, 0.60] | Calibration fraction bounded between 40–90%
μ₁ (covered) | 0.03 | Slow: ≈33 covered observations to shift t_m meaningfully
μ₂ (missed) | 0.50 | Fast: ≈2 misses trigger significant interval widening
α (target) | 1 − coverage | 0.05 for 95%, 0.10 for 90%, 0.20 for 80%, 0.30 for 70%
λ | 0.01 | Slow quantile update to prevent oscillation
All parameters fixed uniformly across all 5 sites — no site-specific tuning. This tests DACP's generalization across diverse flow regimes.

## Slide 20
SECTION 6
Coverage Experiments & Per-Site Results

## Slide 21
Coverage Results: All Sites × All Targets
Site | 70% Target | 80% Target | 90% Target | 95% Target
Bunchgrass Meadow | 68.6% | 77.7% | 84.5% | 86.4%
Easy Pass | 68.6% | 78.2% | 88.2% | 91.8%
Paradise | 64.5% | 75.0% | 87.3% | 89.5%
Swift Creek | 65.0% | 74.5% | 83.2% | 87.3%
Touchet | 64.1% | 75.0% | 85.9% | 90.0%
Coverage Performance Analysis
Coverage performance is moderate compared to the PI-LSTM reference. Systematic undercoverage at higher targets (especially 95%) reflects the LSTM's tendency to underestimate extreme flows — a gap that the PI-LSTM's physics loss partially addresses.
The standard LSTM produces larger, more variable prediction errors during peak events, which challenges DACP's rolling calibration window.

## Slide 22
Average Interval Widths Across Targets
Site | 70% Width | 80% Width | 90% Width | 95% Width
Bunchgrass Meadow | 935.14 cfs | 1034.58 cfs | 1117.44 cfs | 1136.48 cfs
Easy Pass | 12.75 cfs | 16.24 cfs | 21.16 cfs | 27.57 cfs
Paradise | 3.69 cfs | 5.56 cfs | 6.58 cfs | 7.27 cfs
Swift Creek | 2.47 cfs | 3.95 cfs | 5.63 cfs | 6.27 cfs
Touchet | 14.06 cfs | 21.97 cfs | 27.74 cfs | 34.37 cfs
Width Analysis
Width increases monotonically with coverage target as expected. Bunchgrass Meadow shows substantially wider intervals (>1,000 cfs at 95%) reflecting the high variability of its discharge.
Swift Creek maintains the tightest absolute intervals, consistent with its low mean discharge. Relative widths are comparable across sites, showing DACP adapts to each site's scale.

## Slide 23
Per-Site Analysis: Key Findings
Bunchgrass Meadow
R² = 0.476 | RMSE = 559.31 | Cov = 86.4%
Highest-flow site with extreme dynamic range. Log(1+Q) transform applied. Standard LSTM struggles with multi-peak snowmelt patterns without physics constraints.
Easy Pass
R² = 0.613 | RMSE = 13.09 | Cov = 91.8%
Best-performing site for this LSTM. Solar-driven melt captured by GHI feature. The 14-day window adequately captures alpine melt onset dynamics.
Paradise
R² = 0.622 | RMSE = 3.47 | Cov = 89.5%
Rain-on-snow events produce sharp spikes difficult to time precisely. R² acceptable but MRE reflects frequent miss-timing of flash events.
Swift Creek
R² = 0.158 | RMSE = 4.57 | MRE = 0.229 (best) | Cov = 87.3%
Most challenging site with complex mixed hydrology. Best MRE (0.229) despite worst R² — predictions are proportionally close to observed values. DACP coverage falls short at higher targets.
Touchet
R² = 0.381 | RMSE = 20.61 | Cov = 90.0%
Dominated by a single extreme peak event (~672 cfs). Without site-specific Huber loss (used in PI-LSTM), this peak heavily influences training and degrades generalization.

## Slide 24
SECTION 7
Conclusion

## Slide 25
Conclusion
Key Findings
Point Prediction: Standard LSTM achieves R² from 0.158 (Swift Creek) to 0.622 (Paradise). Performance is consistently lower than PI-LSTM, confirming physics-informed training adds meaningful value.
Uncertainty Quantification: DACP achieves reasonable coverage, though systematic undercoverage at 95% target (86–92%) reflects calibrating intervals around a weaker base model.
Physics-Informed Gap: Largest gaps at Bunchgrass (ΔR² = −0.314) and Touchet (ΔR² = −0.512). At Easy Pass, standard LSTM outperforms PI-LSTM by +0.068.
Limitations
• No attention mechanism
• Uniform hyperparameters across all sites
• Short test window (15% ≈ 219 days)
• No site-specific feature selection
• Single loss function for all sites
Future Work
• Site-specific hyperparameter tuning (Optuna)
• Multi-head attention (4 heads)
• Extended input window (30–60 days)
• DACP per-site parameter optimization
• Hybrid physics-informed loss terms

## Slide 26
Thank You
LSTM + DACP: Streamflow Prediction
with Uncertainty Quantification
RIDE Research
May 2026